## Slide 1: Computers, People and the Real World
Martyn Thomas CBE FREng
Livery Company Professor of Information Technology

## Slide 2: Summary
An illustrative story: the failure of the Computer-aided Despatch System of the London Ambulance Service in 1992.
  For the authoritative account, refer to the Inquiry report
Real-world requirements — SocioTechnical systems and what sometimes goes wrong.
The relationships between ways of working and the software that supports them.

## Slide 3: The London Ambulance Service in 1990
The largest ambulance service in the world
Accident and Emergency and Patient Transport for 7m people
600 square miles
More than 5000 patients each day
2000 – 2500 calls each day – 1300 – 1600 are emergency 999
2700 staff (full time equivalents)
300 Accident & Emergency Ambulances
445 Patient Transport Ambulances
500,000 A&E journeys and 1,300,000 Patient Transport journeys each year

## Slide 4: Central Ambulance Control
An urgent call arrives
Location of the emergency is identified, call logged
Duplicated calls are identified and removed
The “best” ambulance to send is identified
The ambulance is contacted and sent
The manual system was inefficient and error-prone
Computerised Command and Control was attempted in the 1980s and abandoned in 1990.
A new Computer-Aided Despatch system was planned …

## Slide 5: Computer-Aided Despatch (CAD)
Computer map display and a gazetteer for phoneboxes and well known places
Automatic location of ambulances
Computer system selects and proposes the nearest ambulances to send and a route, the control operator selects one.
Details are transmitted to the chosen ambulance by data link
Ambulance crew acknowledge the assignment, the CAD system monitors progress
Crew notify their arrival at the emergency, departure to hospital, arrival at hospital, ambulance available for re-assignment.
Very ambitious. No existing system was suitable for use or modification.
Substantial changes to Centre staff and Ambulance crew work processes were required.
CAD System must be dependable and trusted, as manual intervention causes delays, voice calls, network congestion, increased operator workload …

## Slide 6: The CAD Procurement
7 February 1991: call for Expressions of Interest. 35 companies responded.
Required implementation by 8 January 1992
Full proposals from 17 suppliers
  The cheapest by far was from a consortium of Apricot (hardware) , Systems Options (software), and Datatrak (Automatic Vehicle Location).
  £937,463 (about £700k less than the nearest bid!)
  Software development was quoted at £35,000
  The likely underestimate of the complexity was ignored

## Slide 7: 1991
LAS awarded the contract in May 1991 and Systems Options reluctantly became lead contractor.
SO wrote the System Design Specification in June & July
The project slipped, for a variety of reasons.

## Slide 8: 1992
Functional testing and load testing were first attempted in January 1992 (which was the planned full implementation date).
LAS decided on a phased implementation through 1992

## Slide 9: The phased introduction
Up to 26 October 1992, the system was used in a semi-manual fashion
  Calls taken on the CAD system, using computer map
  Incident details printed in the control room
  Best ambulance found by calling the station nearest to the incident
  Mobilisation of the chosen ambulance through CAD

## Slide 10: Problems in 1992
Frequent incomplete status reporting by ambulance crews
  Inadequate training, comms failures, misuse
Inaccurate Datatrak location fixes
  Network “blackspots”
  Faulty equipment or alleged sabotage
  Software errors (eg a failure on every 53rd vehicle)
System could not cope with established working practices (eg a crew taking a different vehicle)

## Slide 11: Continuing Problems in 1992
Communications system overloads
Hardware and software errors
Perhaps, wilful damage to or misuse of Datatrak automatic vehicle location equipment
Failures to notify ambulance status changes or buttons pressed in the wrong order
These and other problems led to the system losing accurate knowledge of vehicle locations (which was essential for continued correct operation).

## Slide 12: Decision to deploy the full CAD system
Despite the remaining faults, the system went live at 7 am on 26 October 1992.
  The control room had been reconfigured , with more terminals and screens and no paper back-up
  The ambulances proposed by the system were mobilised
  It was very difficult for staff to intervene to correct errors

## Slide 13: 26/27 October 1992
Errors continued:
  crew take wrong vehicle or use wrong callsign or a different route, or press status buttons in the wrong order
  Blackspots, transmission failures or equipment problems lead to loss of position or status data.
Consequences:
  The CAD system generated exceptions, allocated the wrong ambulance, sent duplicate ambulances, delays increased and led to more call-backs and exception messages, operators became overloaded, there were long delays to answering calls and to reaching patients. Claims that 20 to 30 people died were not substantiated.

## Slide 14: The afternoon of 27 October
The decision was taken to revert to semi-manual operation
  Calls taken on the CAD system, using computer map
  Incident details printed in the control room
  Best ambulance found by calling the station nearest to the incident
  Mobilisation of the chosen ambulance through CAD
This worked fairly well until 4 November, as extra staff had been added

## Slide 15: 2 am on 4 November 1992
The CAD system slowed, then crashed. Re-booting workstations failed to clear the problem.
  The server had failed because of a coding error in the software that caused a memory leak.
  The backup server was not designed to be used with the semi-manual configuration and had never been tested.
LAS reverted to a fully manual, paper-based system.

## Slide 16: Subsequent events
The LAS Chief Executive resigned a few days later
A public Inquiry was set up and reported in February 1993 (ISBN 0-905133-70-6).
The report is available online:
  http://www0.cs.ucl.ac.uk/staff/A.Finkelstein/las/lascase0.9.pdf

## Slide 17: Lessons from LASCAD
The CAD system was overambitious and the timetable was unachievable.
The bidder who least understands the complexity of a requirement is likely to put in the lowest bid.
The LASCAD architecture was too prone to cascade failures when data was wrong.
  Error rates overloading operators is a well-known problem (eg TMI)
It is a mistake to use a computer system to impose new work processes on under-trained or reluctant staff.
  Front-line staff are often best placed to judge what is practical
“In any system implementation the people factor is as important, and arguably more important, than the technical infrastructure” [LAS Inquiry Report, paragraph 3107, page 39]

## Slide 18: Front-line staff optimise the way they work
To improve efficiency, to reduce errors, or just because it is easier or gives job satisfaction
  The reasons may not be written down – or even known to current staff. It’s the way we do it
Some of the LASCAD problems were caused by staff resistance to changes to work processes
  Perhaps for good reasons …
It is important to understand current work processes before trying to change them!

## Slide 19: The Smartcard dispute in NPfIT
Electronic Patient Records are sensitive personal data.
NPfIT introduced role-based access control to maximise privacy.
Smartcards were used to identify staff and their role in treating the patient
Doctors were instructed not to share logins
  But switching users involved logging out, logging in and navigating back to the patient’s records
  Staff knew this was often impractical

## Slide 20
Computer-based Systems involve
People
Working with
Technology

## Slide 21: Sociotechnical Systems a perspective that recognises that:
Requirements are statements about the real world, not about the technology
computer systems are almost always there to support the actions of humans, not the reverse
the humans whose behaviour can affect the achievement of the requirements are part of the system
... and their behaviour is affected by their culture, laws, physical environment, habits, ethics and training

## Slide 22: Training: vital for dependable systems! A true story of the university Provost’s PA
IT support noticed that the Provost’s monthly newsletter was taking longer and longer to deliver.
An email came round ….
  “Please delete all email from the Provost”
The Provost’s PA had habitually started every new Word document by opening the previous one, deleting the contents and typing the new one.
  With tracked changes turned on
  So each document contained a copy of every previous letter that the Provost had ever sent, to anyone …

## Slide 23: Don’t assume how people will behave – check! Computer-assisted cancer diagnosis
One human reader, supported by computer image analysis
An advisory system was not considered safety-critical
Research showed that the system helped the less good readers but led to more errors by expert readers.
For details, see references in the lecture transcript

## Slide 24: Even experts get it wrong

## Slide 25: As reported by The Independent …
A Microsoft computer program that learns how to speak English by interacting with the public on Twitter has been taken offline after it quickly took on the identity of a foul-mouthed genocidal Nazi.
The methods of artificial intelligence used by the “chatbot” named Tay appeared to have been exploited by far-right racists and conspiracy theorists.
Within 24 hours of being introduced to the internet, it went from tweeting “hellooo world!” to writing: “Bush did 9/11 and Hitler would have done a better job than the monkey we have now. Donald Trump is the only hope we’ve got.”
“As it learns, some of its responses are inappropriate and indicative of the types of interactions some people are having with it,” [Microsoft] said.

## Slide 26: Too often, the focus is on the technology, not the real requirement
Image Credit: Veronica Therese, Wikimedia Commons

## Slide 27: “There is no such thing as an IT Project”
(almost) every significant “IT Project” is actually a business change project that is enabled and supported by one or more IT systems.
Business processes are expensive to change.
The business changes take at least as long and cost as much as the new IT system, and need at least as much planning and management

## Slide 28: Software Packages are packaged business processes
Changing a package to fit the way you want to work can cost more than writing new software
  Modifications will need reimplementation for every new release of the base package
  Delays to updates may risk cyberattacks
  Don’t expect suppliers to add your changes to their software packages …. Even if they promised to “consider it”

## Slide 29: Software Packages are packaged business processes
Changing how you work to fit in with the package may be difficult or impossible
  US health-care packages that focus on billing
  Customer billing packages that do not reflect local laws
  University administration packages that do not recognise Oxbridge college relationships

## Slide 30: Conclusions
Requirements exist in the real world, not at the boundary of a computer system.
Most computer systems interact with people: the sociotechnical view is that the people and the IT are two components of a larger system
Designing that larger system is the real task. It can be done rigorously (see references).
The experts in any work process are usually the people who have been carrying it out.

## Slide 31: Further Cyberliving Lectures this year
3 May Cybersecurity
14 June Big Data: The Broken Promise of Anonymisation
18 October: Are you the customer or the product?
It has been said that if you are not paying for a service, then you are the product, not the customer. To what extent is this true for free software, social networking, and other free IT services and products? If we are the product, are we selling ourselves too cheaply? Who is tracking us, and how? How can we retain control?

## Slide 32: Please join in the discussions
Please share your views on http://cyberliving.uk and by using the Twitter hashtag #cyberliving